## Slide 1
Image Enhancement-I
Lecture-3 (24th August 2021)

## Slide 2
Topics covered till now:
Image Acquisition Process
Image sampling and quantization
Basic relationship between pixels
  Neighbors
  Connectivity
  Path
  Region & Adjacency
  Boundary
  Distance Measure

## Slide 3
Image Sampling and Quantization
Image has two components: co-ordinates and amplitude.
Image at lens focal plane is continuous.
To digitize an image, both co-ordinates and amplitude needs to be digitized.
Digitizing the co-ordinate values sampling
Digitizing the amplitude values  quantization

## Slide 4
Quantization levels [0, L-1]
L=2k
k no. of bits per channel
How many quantization levels can we have?

## Slide 5
Images with varying intensity levels ‘L’

## Slide 6
The number ‘b’ of bits required to store a M × N digitized image
b = M × N × k
k representing k bit image

## Slide 7
Neighbors of a pixel p at coordinates (x,y)
4-neighbors of p, denoted by N4(p):
(x-1, y), (x+1, y), (x,y-1), and (x, y+1).
4 diagonal neighbors of p, denoted by ND(p):
(x-1, y-1), (x+1, y+1), (x+1,y-1), and (x-1, y+1).
8 neighbors of p, denoted N8(p)
N8(p) = N4(p) U ND(p)
Neighborhood

## Slide 9
Connectivity
Let V be the set of gray levels used to define connectivity for two pixels p and q, three types of connectivity are defined.
  4-connectivity: p,q ϵ V and p ϵ (q)
  8-connectivity: p,q ϵ V and p ϵ (q)
  M-connectivity (mixed connectivity): p,q ϵ V
  i. q ϵ (p) or
  ii. q ϵ (p) and (p) ∩ (q) = ϕ
0 | 1 | 1
0 | 1 | 0
0 | 0 | 1
0 | 1 | 1
0 | 1 | 0
0 | 0 | 1
4-connectivity
8-connectivity
M-connectivity
Eg. V={1}
p
q
0 | 1 | 1
0 | 1 | 0
0 | 0 | 1

## Slide 10
A (digital) path (or curve) from pixel p with coordinates (x0, y0) to pixel q with coordinates (xn, yn) is a sequence of distinct pixels with coordinates
(x0, y0), (x1, y1), …, (xn, yn)
where (xi, yi) and (xi-1, yi-1) are adjacent for 1 ≤ i ≤ n.
Here n is the length of the path.
If (x0, y0) = (xn, yn), the path is closed path.
We can define 4-, 8-, and m-paths based on the type of adjacency used.
Path
p
q

## Slide 11
We call ‘R’ a region of the image if R is a connected set.
Two regions, and are said to be adjacent if their union forms a connected set.
Regions that are not to be adjacent are said to be disjoint.
Region 1
Region 2
1 | 1 | 1
1 | 0 | 1
0 | 1 | 0
0 | 0 | 1
1 | 1 | 1
1 | 1 | 1
8-adjacency
4-adjacency
8-adjacency
m-adjacency
Region & Adjacency

## Slide 12
0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
Black- background
White- foreground
8 - connectivity
The boundary of the region R is the set of pixels in the region that have one or more neighbors that are not in R (background).
Boundary

## Slide 13
0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
Black- background
White- foreground
8 - connectivity
4 - connectivity
MATLAB: B = bwboundaries (binary_image,connectivity)

## Slide 14
The Euclidean Distance between p and q is defined as:
De (p,q) = [(x – s)2 + (y - t)2]1/2
q (s,t)
De (p,q)
p (x,y)
Euclidean Distance

## Slide 15
The D4 distance (also called city-block distance) between p and q is defined as:
D4 (p,q) = | x – s | + | y – t |
City-Block Distance
p (x,y)
q (s,t)
D4

## Slide 16
The D8 distance (also called chessboard distance) between p and q is defined as:
D8 (p,q) = max(| x – s |,| y – t |)
Chessboard Distance
p (x,y)
q (s,t)
D8(b)
D8(a)
D8 = max(D8(a) , D8(b))

## Slide 17
Today’s lecture
Image enhancement techniques
Intensity transformation function
  Image negative
  Log transformation
  Gamma transformation
Piecewise linear transformation
  Contrast stretching
  Intensity level slicing
Histogram processing

## Slide 18
Image enhancement techniques
Objective – process an image so that the result is more suitable than the original image for a specific application. (improve the quality)
Methods:
Spatial Domain direct manipulation of pixels of the image
Frequency Domain modifying the frequency transformed image

## Slide 19
These techniques operate directly on the pixels.
More efficient computation and requires less processing resources to implement
Spatial Domain Process is defined by g(x,y)=T[f(x,y)]
T is an operator on input image defined over a neighborhood of point (x,y)
INPUT IMAGE
OUTPUT IMAGE
Spatial Domain

## Slide 20
1. Image Negative
Let the image has an intensity level in the range [0 L-1], then the intensity transformation is given by s=L-1-r
0
L-1
L-1
r
s=T(r)
Input intensity
Output intensity
L=intensity levels

## Slide 21
2. Log Transformation
For an image having intensity ranging from [0 L-1], log transformation is given by s=c log(1+r) , where c is a constant.
r
0
L-1
L-1
s=T(r)
Input intensity
Output intensity
Maps the narrow range of low intensity values of input levels to wider range of output levels.
Higher range of high intensity input levels is mapped to narrow range of output levels.

## Slide 22
3. Power-law (Gamma) Transformation
This has the basic form s=c rγ ,where c and γ are positive constants
Plot for c=1
Dark input  bright output when gamma<1
Same input and output at gamma=1
bright input  dark output when gamma >1

## Slide 23
Gamma correction is very important when to reproduce an image exactly on a display system.
MRI of fractured human spine
Result of a transformation for γ=0.3

## Slide 24
MRI of fractured human spine
Result of a transformation for γ=0.6
Result of a transformation for γ=0.4
Result of a transformation for γ=0.3

## Slide 25
Arial image
Result of a transformation for c=1 and γ=3

## Slide 26
Result of a transformation for c=1 and γ=4
Result of a transformation for c=1 and γ=5

## Slide 27
s = T(r)
0
0
L-1
L-1
Input intensity level, r
output intensity level, s
dark
light
dark
light
4. Contrast stretching
Expand a range of intensities at input to desired range at output.
Sometimes, image viewed in the screen is very dark (poor contrast).
Poor illumination
dynamic range of the sensor is very small. (capacity to record min and max intensity value)
aperture of lens is not properly set.

## Slide 28
Contrast stretching
0
0
L/4
L/4
L/2
3L/4
L-1
L/2
3L/4
L-1
Input intensity level, r
output intensity level, s
(r1,s1)
(r2,s2)
T(r)
Controls the shape of the transformation function

## Slide 29
0
0
L/4
L/4
L/2
3L/4
L-1
L/2
3L/4
L-1
Input intensity level, r
output intensity level, s
(r1,s1)
(r2,s2)
T(r)
Contrast stretching
Suppose r1=s1 and r2=s2
0
0
L/4
L/4
L/2
3L/4
L-1
L/2
3L/4
L-1
output intensity level, s
(r1,=s1)
(r2,= s2)
T(r)
Input intensity level, r

## Slide 30
Contrast stretching
0
0
L/4
L/4
L/2
3L/4
L-1
L/2
3L/4
L-1
Input intensity level, r
output intensity level, s
(r1,s1)
(r2,s2)
T(r)
Suppose r1=r2 and s1=0 and s2=L-1
0
0
L/4
L/4
L/2
3L/4
L-1
L/2
3L/4
L-1
Input intensity level, r
output intensity level, s
T(r)
(r1)
(r2)

## Slide 31
Contrast stretching (Example)

## Slide 33
Contrast stretching (Example)

## Slide 34
5. Intensity Level slicing
Highlighting specific range of intensities.
Example :
    Enhancing features such as masses of water in the satellite imagery
    Enhancing flaws in X-ray images.
    Contrast stretching: whole image intensity is affected

## Slide 35
0
L-1
L-1
T(r)
r
s
L-1

## Slide 36
0
L-1
L-1
T(r)
r
s

## Slide 37
Intensity Level slicing (Example)

## Slide 38
What is histogram
Histogram based techniques
  Histogram equalization
  Histogram specification/matching/modification
6. Histogram Processing

## Slide 39
What is a histogram?
Gives a global description of an appearance of an image.
 number of pixels having an intensity value .
Intensity values
Normalized histogram
n  total number of pixels.

## Slide 40
Dark image
Darker region

## Slide 41
Bright image
Lighter region

## Slide 42
Low contrast image
Neither dark nor bright

## Slide 43
High contrast image
Detailed image

## Slide 44
  Histogram gives global appearance not the content of image.
  Histogram based techniques modifies the histogram of image to appear in the way we want.
  Histogram equalization
  Histogram specification/matching/modification

## Slide 45
Histogram equalization
Normalized histogram
Transformation function for histogram equalization
(cumulative)
Intensity of the output image after equalization

## Slide 46
R (input intensity values) | No. of pixels | P(r) (normalized histogram) | T(r) CDF | s’ (output intensity values)
0 | 2 | 0.05 | 0.05 | 0
1 | 2 | 0.05 | 0.1 | 0
2 | 0 | 0 | 0.1 | 0
3 | 0 | 0 | 0.1 | 0
4 | 0 | 0 | 0.1 | 0
5 | 6 | 0.15 | 0.25 | 1
6 | 14 | 0.35 | 0.60 | 4
7 | 16 | 0.40 | 1 | 7
 | Sum=40 |  |  | 

## Slide 47
R (input intensity values) | No. of pixels | P(r) (normalized histogram) | T(r) CDF | s’ (output intensity values)
0 | 2 | 0.05 | 0.05 | 0
1 | 2 | 0.05 | 0.1 | 0
2 | 0 | 0 | 0.1 | 0
3 | 0 | 0 | 0.1 | 0
4 | 0 | 0 | 0.1 | 0
5 | 6 | 0.15 | 0.25 | 1
6 | 14 | 0.35 | 0.60 | 4
7 | 16 | 0.40 | 1 | 7
 | Sum=40 |  |  | 

## Slide 48
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
input | 2 | 2 | 0 | 0 | 0 | 6 | 14 | 16
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Column1 | 4 | 6 | 0 | 0 | 14 | 0 | 0 | 16

## Slide 49
Input histogram
Target histogram
Histogram matching
Transformation matrices

## Slide 50
R (input intensity values) | Pr(r) (histogram) | T(r) = s | Pz(z) | G(z) | Z’ (output intensity)
0 |  |  |  |  | 
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 

## Slide 51
R (input intensity values) | Pr(r) (histogram) | T(r) = s | Z | Pz(z) | G(z) | Z’ (output intensity)
0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0.1 | 0.1 | 1 | 0.1 | 0.1 | 1
2 | 0.1 | 0.2 | 2 | 0.2 | 0.3 | 2
3 | 0.3 | 0.5 | 3 | 0.4 | 0.7 | 
4 | 0 | 0.5 | 4 | 0.2 | 0.9 | 
5 | 0 | 0.5 | 5 | 0.1 | 1 | 
6 | 0.4 | 0.9 | 6 | 0 | 1 | 
7 | 0.1 | 1 | 7 | 0 | 1 | 

## Slide 52
R (input intensity values) | Pr(r) (histogram) | T(r) = s | Z | Pz(z) | G(z) | Z’ (output intensity)
0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0.1 | 0.1 | 1 | 0.1 | 0.1 | 1
2 | 0.1 | 0.2 | 2 | 0.2 | 0.3 | 2
3 | 0.3 | 0.5 | 3 | 0.4 | 0.7 | 3
4 | 0 | 0.5 | 4 | 0.2 | 0.9 | 3
5 | 0 | 0.5 | 5 | 0.1 | 1 | 3
6 | 0.4 | 0.9 | 6 | 0 | 1 | 4
7 | 0.1 | 1 | 7 | 0 | 1 | 5